CodeSnip User Database XML Data File Format
The user defined snippets database displayed and edited by CodeSnip is stored in an XML file that references a series of associated data files that contain snippets' source code.
# XML File Format
The XML data file is named database.xml. There are four different file formats. Each format has a version number from 1 to 4. Files are UTF-8 encoded, with no byte order mark.
## Differences between file formats
Version 1	First version of file.
Version 2	The following tags are no longer supported / codesnip-data/routines/routine/comments / codesnip-data/routines/routine/credits / codesnip-data/routines/routine/credits-url / The following tag was introduced: / codesnip-data/routines/routine/extra / The markup stored in the extra tag is REML v1. / Note: Readers of version 1 files must generate REML markup from the comments, credits and credits-url tags to mimic the data normally provided by the extra tag.
Version 3	The following tag is no longer supported: / codesnip-data/routines/routine/standard-format / The following tag was introduced: / codesnip-data/routines/routine/kind / Note: Readers of v1 and v2 files should map a standard-format value of 0 to a kind of “freeform” and a standard-format value of 1 to a kind of “routine”. / The version of REML supported by the codesnip-data/routines/routine/extra tag was updated to v2.
Version 4	The version of REML supported by the codesnip-data/routines/routine/extra tag was updated to v3.

## Supported XML Tags
Each tag is explained in the table below.
Tag	Description
<?xml?>	XML processing instruction. / Attributes are: / version: XML version. Always set to “1.0”.
<codesnip-data>	Parent node for whole file. / Attributes are: / watermark: Identifies file as correct type – always set to 531257EA-1EE3-4B0F-8E46-C6E7F7140106 / version: Identifies version of file. Determines which tags are valid and rules concerning content. Valid versions are 1..4
<categories>	Contains list of all categories.
<category>	Contains information about a category. / Attributes are: / id: Internal (unique) id of category
<description>	Description of category.
<cat-routines>	Contains list of name of all snippets in category. Omitted if there are no snippets in category.
<pascal-name>	Contains name of a snippet. One per each snippet in category. / Name must begin with an English language letter or the underscore.
<routines>	Contains a list of all user defined snippets.
<routine>	Contains information about a snippet. One per snippet. / Attributes are: / name: Name of snippet. Name must begin with an English language letter or the underscore.
<cat-id>	Id of category to which snippet belongs.
<description>	Description of snippet
<source-code>	Name of file containing snippet's source code. No path information included.
<comments>	version 1: Additional comments about snippets. / version 2 and later: Not supported.
<credits>	version 1: Credits for snippets. May contain a single piece of text, delimited by “[“ and “]” that can form a hyperlink. URL for the hyperlink is provided in <credits-url>. / version 2 and later: Not supported.
<credits-url>	version 1: URL required by <credits> tag. Present only if <credits> requires a hyperlink. / version 2 and later: Not supported.
<extra>	version 1: Not supported. / version 2 and later: Additional information about a snippet. Content is REML markup. / version 2 indicates REML v1 version 3 indicates REML v2 version 4 indicates REML v3.
<standard-format>	versions 1 and 2: Flag indicating if snippet is in “standard format”. Value of 1 indicates true and 0 indicates false. / version 3 and later: Not supported.
<kind>	versions 1 and 2: Not supported. / version 3 and later: Value indicating kind of snippet. Permissible values are: “freeform”, “routine”, “type” & “snippet”.
<compiler-results>	Contains a list of compile results for the snippet.
<compiler-result>	Entry for each known compile result. / Attribute is: / id: identifies compiler – one of “d2”, “d3”, “d4”, “d5”, “d6”, “'d7”', “d2005”, “d2006”, “d2007”, “d2009”, “d2010”, “dXE” & “fpc”. / Values are “Y”, “N”, “W” or “Q”. Omitting a compiler is equivalent to specifying “Q”.
<units>	List of required units.
<pascal-name>	Name of a unit within unit list.
<depends>	List of required snippets.
<pascal-name>	Name of a snippet within depends list. / Name must begin with an English language letter or the underscore.
<xref>	List of cross-referenced snippets.
<pascal-name>	Name of a snippet within cross-reference list. / Name must begin with an English language letter or the underscore.

# Source Code Data File Format
Numbered data files with .dat extensions are used to store the source code of each snippet as plain text.
These files are encoded with the system's default encoding.