CodeSnip Export XML Data File Format
User defined snippets can be exported from the program for importing into another program or for submitting to the online database. Exported data is stored in a single XML file.
There are five different file formats. Each format has a version number from 1 to 5. Files are UTF-8 encoded. with no byte order mark.
# Differences between file formats
Version 1	First version of file.
Version 2	The following tags are no longer supported / codesnip-export/routines/routine/comments / codesnip-export/routines/routine/credits / codesnip-export/routines/routine/credits-url / The following tag was introduced: / codesnip-export/routines/routine/extra / The markup stored in the extra tag is REML v1. / Note: Readers of version 1 files must generate REML markup from the comments, credits and credits-url tags to mimic the data normally provided by the extra tag.
Version 3	The following tag is no longer supported: / codesnip-export/routines/routine/standard-format / The following tag was introduced: / codesnip-export/routines/routine/kind / Note: Readers of v1 and v2 files should map a standard-format value of 0 to a kind of “freeform” and a standard-format value of 1 to a kind of “routine”. / The version of REML supported by the codesnip-export/routines/routine/extra tag was updated to v2.
Version 4	The version of REML supported by the codesnip-export/routines/routine/extra tag was updated to v3.
Version 5	The file encoding was explicitly set to “UTF-8”. by setting the encoding attribute of the XML processing instruction to this value. / The value of the codesnip-export/routines/routine tag's name attribute can now begin with any character that is a valid first character of a Unicode Pascal identifier. Previously the first character of the attribute had to be one of 'A'..'Z', 'a'..'z' or '_'.

# Supported XML Tags
Each XML tag is explained in the table below.
Tag	Description
<?xml?>	XML processing instruction. / Attributes are: / version: XML version. Always set to “1.0”. / encoding: Character encoding for XML file. / versions 1..4: Attribute not provided. / version 5: Always set to “UTF-8”.
<codesnip-export>	Parent node for whole file. / Attributes are: / watermark: Identifies file as correct type – always set to B46969D4-D367-4F5F-833E-F165FBA78631 / version: Identifies version of file. Determines which tags are valid and rules concerning content. Valid versions are 1..5.
<prog-version>	Version of program that generated the file, as a dotted quad with format N.N.N.N where N is a non-negative integer.
<user-info>	Contains information about user who created the file (omitted for normal exports – included for submissions to the online database).
<name>	User name.
<email>	User's email address.
<comments>	Any comments provided by user.
<routines>	Contains a list of all exported snippets.
<routine>	Contains information about an exported snippet. One per snippet. / Attribute is: / name: name of snippet. / versions 1..4: Name must begin with an English language letter or the underscore. / version 5: Name can begin with any character that is valid as the first character of a Unicode Pascal identifier.
<description>	Description of snippet
<source-code-text>	Snippet source code.
<comments>	version 1: Additional comments about snippets. / version 2 and later: Not supported.
<credits>	version 1: Credits for snippets. May contain a single piece of text, delimited by “[“ and “]” that can form a hyperlink. URL for hyperlink provided in <credits-url>. / version 2 and later: Not supported.
<credits-url>	version 1: URL required by <credits> tag. Present only if <credits> requires a hyperlink. / version 2 and later: Not supported.
<extra>	version 1: Not supported. / version 2 and later: Additional information about a snippet. Content is REML markup. / version 2 indicates REML v1 version 3 indicates REML v2 version 4 indicates REML v3.
<standard-format>	versions 1 and 2: Flag indicating if snippet is in “standard format”. Value of 1 indicates true and 0 indicates false. / version 3 and later: Not supported.
<kind>	versions 1 and 2: Not supported. / version 3 and later: Value indicating kind of snippet. Permissible values are: “freeform”, “routine”, “type” & “snippet”.
<compiler-results>	Contains a list of compile results for the snippet.
<compiler-result>	Entry for each known compile result. Attribute is: / id: identifies compiler – one of “d2”, “d3”, “d4”, “d5”, “d6”, “'d7”', “d2005”, “d2006”, “d2007”, “d2009”, “d2010” & “fpc”. / Values are “Y”, “N”, “W” or “Q”. Omitting a compiler is equivalent to specifying “Q”.
<units>	List of required units.
<pascal-name>	Name of a unit within unit list. / Must be a valid Pascal identifier.
<depends>	List of required snippets.
<pascal-name>	Name of a snippet within depends list. / versions 1..4: Name must begin with an English language letter or the underscore. / version 5: Name can begin with any character that is valid as the first character of a Unicode Pascal identifier.
<xref>	List of cross-referenced snippets.
<pascal-name>	Name of a snippet within cross-reference list. / versions 1..4: Name must begin with an English language letter or the underscore. / version 5: Name can begin with any character that is valid as the first character of a Unicode Pascal identifier.